## Slide 1
CIRCUIT CONNECTION SCHEMATIC & PIN INTERFACE MAP STM32F446RE (NUCLEO-64) • SMART CLASSROOM & PRESENTATION CONTROLLER
STM32 NUCLEO-F446RE
ARM Cortex-M4 @ 180 MHz • 12-Bit ADC • TIM3 PWM • I2C1 • USART2
--- [LEFT HEADERS: ANALOG & INPUTS] ---
◄ PA0 (A0) : ADC1_IN0 (LDR Light Sensor)
◄ PA1 (A1) : ADC1_IN1 (LM35 Temp Sensor)
◄ PA4 (A2) : GPIO IN (PIR Motion Sensor)
◄ PB4 (D5) : GPIO IN (Manual Switch / Pull-Up)
◄ PC13 (B1) : User Button (Baseline Recalibrate)
--- [RIGHT HEADERS: PWM & ACTUATORS] ---
► PB0 (D3) : Front Light Relay 1 (0% Glare Shield)
► PB1 (D6) : Mid Light Relay 2 (20% Note Dim)
► PB2 (D7) : Back Light Relay 3 (20% Note Dim)
► PB5 (D4) : Exhaust Fan Relay 4 (Trigger >28°C)
► PA6 (D12) : TIM3_CH1 PWM (SG90 Servo 0°-180°)
► PA7 (D11) : GPIO OUT (Warning Piezo Buzzer)
--- [BUS HEADERS: I2C & SERIAL] ---
► PB8 (D15) : I2C1_SCL (16x2 LCD Clock)
► PB9 (D14) : I2C1_SDA (16x2 LCD Data)
► PA2 / PA3 : USART2 TX/RX (115200 Baud Console)
LDR LIGHT SENSOR MODULE
Ambient Lux Measurement
• VCC --> (+) 3.3V Rail • GND --> (-) GND Rail • AO ===================> PA0 (A0) [ADC1_IN0]
LM35 TEMPERATURE SENSOR
Linear 10 mV / °C Output
• Pin 1 (+Vs) --> (+) 3.3V Rail • Pin 3 (GND) --> (-) GND Rail • Pin 2 (Vout) ===============> PA1 (A1) [ADC1_IN1]
PIR MOTION SENSOR (HC-SR501)
30-Second Vacancy / Occupancy Detection
• VCC --> (+) 5.0V Rail • GND --> (-) GND Rail • OUT ===================> PA4 (A2) [Digital In]
MANUAL OVERRIDE SWITCH
Force Presentation Mode Toggle
• Pin 1 --> (-) GND Rail • Pin 2 =================> PB4 (D5) [Pull-Up In] [ Open = Auto Mode | Closed to GND = Presentation ]
4-CHANNEL 5V RELAY MODULE
Optocoupler Isolated AC/DC Load Controller
• VCC --> (+) 5.0V Rail | GND --> (-) GND • IN1 <=================== PB0 (D3) [Front Light] • IN2 <=================== PB1 (D6) [Mid Light] • IN3 <=================== PB2 (D7) [Back Light] • IN4 <=================== PB5 (D4) [Exhaust Fan] • Relay 1: Front Light OFF (0% Glare Shield) • Relay 2 & 3: Mid/Back Lights (20% Note Dimming) • Relay 4: Fan ON when Temp > 28.0°C
SG90 SERVO MOTOR (WINDOW BLINDS)
Motorized Glare Shielding (50 Hz PWM)
• Red (VCC) --> (+) 5.0V Rail • Brown (GND) --> (-) GND Rail • Orange (PWM) <============== PA6 (D12) [TIM3_CH1] [ 0° = Blinds Open | 90°/180° = Blinds Closed ]
BUZZER & 16x2 I2C LCD DISPLAY
Audio Warning Chime & Visual Telemetry
• Buzzer (+) <============== PA7 (D11) [GPIO] • LCD SCL (D15) <============= PB8 (I2C1_SCL) • LCD SDA (D14) <============= PB9 (I2C1_SDA) • LCD VCC / GND --> (+) 5V / (-) GND (Addr: 0x27)