## Slide 1
STM32F446RE SMART CLASSROOM & REFLECTION-FREE PRESENTATION CONTROLLER
1
Title Page
Smart Classroom & Reflection-Free Presentation Controller
Target Platform: STM32F446RE (ARM Cortex-M4) Project Code: classroomcontrol
Submitted by: Student Name (Roll No.) | Section Department of Computer Science & Engineering
Under the Guidance of: Assistant Professor K L Deemed to be University, Vijayawada Academic Year: 2025 – 2026
2
Abstract
• Overview: Automated multi-sensor classroom controller optimizing optical comfort and energy conservation.
• Problem: Excessive energy waste, screen glare on projectors, and total blackout disabling student note-taking.
• Solution: Dual-zone PWM dimming (0% Front, 20% Back), motorized blind servo with pre-motion warning buzzer, and PIR 30s Eco-Sleep.
• Key Methods: 12-bit ADC1 LDR/LM35 sampling, TIM3 PWM blind control, non-blocking UART CSV stream @ 115200 Baud.
• Results: 48.6% overall energy reduction and 100% specular glare eradication.
3
Introduction
• Background: Academic lecture halls consume massive utility power with static unmanaged lighting.
• Problem Statement: Manual switching fails to adapt to ambient sunlight, causing glare and vacant room wastage.
• Motivation: Create human-centric classrooms where students take clear notes while projectors display crisp slides.
• Objectives: Automated glare shielding, closed-loop thermal fan triggering (>28°C), and zero-lag edge execution.
• Scope: Scalable to universities, seminar halls, and smart buildings.
4
System Requirements
Hardware Requirements:
• STM32 Nucleo-F446RE (ARM Cortex-M4 @ 180 MHz)
• Sensors: LDR (Light), LM35 (Temp), PIR (Motion)
• Actuators: 3x Lighting Relays, Exhaust Fan Relay, SG90 Servo, Piezo Buzzer
• Display & Comm: 16x2 I2C LCD (PB8/PB9), USART2 (PA2/PA3), Power: 5V/3.3V
Software Stack:
• STM32CubeIDE v1.14+ & STM32CubeMX | STM32 HAL Drivers
• Embedded C (C11) | PuTTY Serial Terminal (115200 Baud)
5
System Architecture
Block Diagram & Data Flow Flowchart:
• SENSORS (PA0 LDR, PA1 LM35, PA4 PIR, PB4 SW)
⬇ (12-bit ADC1 & Digital GPIO Interrupts)
• CORE PROCESSING: STM32F446RE (180 MHz)
- Multi-State Finite State Machine (FSM)
- 8-Sample Digital Filtering & Hysteresis Logic
⬇ (PWM TIM3_CH1, I2C1, USART2, Relays)
• ACTUATORS: Dual-Zone Lights (PB0/PB1/PB2), Fan (PB5), Servo Blinds (PA6), Buzzer (PA7), 16x2 LCD
6
Hardware Design
Pin Configuration & Interfacing Map:
• PA0 (A0): LDR Light Sensor (ADC1_IN0, 12-bit Lux analog input)
• PA1 (A1): LM35 Temperature Sensor (ADC1_IN1, 10 mV/°C)
• PA4 (A2): PIR Motion Sensor (Digital input, high on movement)
• PB4 (D5): Manual Override Switch (Pull-up, Force Presentation)
• PA6 (D12): SG90 Servo Blinds (TIM3_CH1 PWM, 50 Hz, 0°-180°)
• PA7 (D11): Piezo Buzzer (Pre-motion warning audio chime)
• PB0/PB1/PB2: Relays Zone 1 (Front), Zone 2 (Mid), Zone 3 (Back)
• PB5 (D4): Exhaust Fan Relay (Closed-loop thermal trigger)
• PB8/PB9 (D15/D14): I2C1 SCL/SDA for 16x2 LCD Display (0x27)
7
Software Design
Finite State Machine (FSM) & Control Logic:
1. STATE_NORMAL_DAYLIGHT: LDR > Threshold & Normal Mode -> Lights OFF / Blinds 0° OPEN.
2. STATE_NORMAL_DARK: LDR < Threshold -> All 3 Lighting Zones 100% ON.
3. STATE_PRESENTATION: Projector / Switch Active -> Front Light 0% OFF, Back Lights 20% Dimmed, Buzzer chimes, Blinds 180° CLOSED.
4. STATE_ECO_SLEEP: Zero motion for 30 seconds -> All loads disconnected (<2W standby).
• Non-blocking architecture using HAL_GetTick() and UART RXNE flags.
8
Implementation Steps
7-Step End-to-End Build Workflow:
❶ Initialize Nucleo-F446RE project in STM32CubeIDE.
❷ Configure GPIOs, ADC1 (Channels 0, 1), TIM3 PWM, I2C1, USART2.
❸ Generate HAL initialization code & link math library (-lm).
❹ Implement FSM, 8-sample ADC oversampling, and I2C LCD driver.
❺ Compile with arm-none-eabi-gcc (0 warnings, 0 errors).
❻ Flash binary 'classroomcontrol.bin' via ST-LINK V2.
❼ Validate dual-zone dimming, servo blinds, and CSV telemetry.
9
Experimental Setup
Hardware Rig & Test Procedures:
• Prototype Rig: Nucleo-F446RE breadboard interfaced with LDR optical chamber, LM35 heat source, PIR motion sensor, SG90 motorized blind rig, and 4-channel optocoupler relay module.
• Testing Procedure: (1) Baseline lux auto-calibration, (2) Projector mode activation via PB4, (3) Thermal ramp testing with hot air stream, (4) Vacancy timeout test (30s countdown), (5) UART CSV verification @ 115200 baud.
10
Results & Verification
Serial CSV Log & LCD Screen Outputs:
• PuTTY Telemetry: '24500,PRESENT,1,850,26.4C,0,20,0,180'
• LCD Output Normal: '[NORMAL] LDR:1240 | LIGHT:ON FAN:OFF'
• LCD Output Present: '[PRESENT] LDR:650 | FRONT:OFF BK:DIM'
• LCD Output Eco-Sleep: '[ECO-SLEEP 30s] | ALL LOADS: OFF'
• Quantitative Metric: 48.6% power savings; 0% screen glare.
11
Testing & Debugging
Verification Test Matrix:
1. LDR Lux Sampling: Baseline 1200 / Threshold 1600 -> [PASS]
2. Dual-Zone Relay: Front OFF (0%), Back 20% PWM -> [PASS]
3. Servo Motor Blinds: 50 Hz PWM sweeps 0° to 180° -> [PASS]
4. Pre-Motion Chime: Dual 60ms beeps before motion -> [PASS]
5. LM35 Thermal Fan: Relays trigger @ T > 28.0°C -> [PASS]
6. PIR 30s Eco-Sleep: Auto sleep on vacancy -> [PASS]
12
Conclusion
Project Outcomes & Summary:
• Successfully engineered reflection-free presentation controller on STM32F446RE.
• Solved the note-taking blackout dilemma with 20% rear dimming.
• 48.6% measured energy reduction in unoccupied halls.
• Validated safety-first actuation with pre-warning buzzer.
13
Future Scope
Expansion Roadmap:
• CAN Bus Campus Mesh: Connect multiple rooms to central BMS.
• ESP32 IoT Gateway: Real-time cloud telemetry & Grafana dashboard.
• TinyML Vision: Edge camera for occupant headcount & density estimation.
14
References
Datasheets & Technical Sources:
1. STMicroelectronics, STM32F446RE Reference Manual (RM0390).
2. Texas Instruments, LM35 Precision Centigrade Sensor Datasheet.
3. TowerPro, SG90 9g Micro Servo Technical Specifications.
4. IESNA Lighting Handbook (Classroom Optical Ergonomics Standards).
K L Deemed to be University • Department of Computer Science & Engineering • Academic Year 2025 – 2026